CENTRAL CAROLINA COMMUNITY COLLEGE

1801 NASH ST. SANFORD NC 27330

ENERGY EFFICENCY COMMINITY BLOCK GRANT PROGRAM

RFP # 43-A-2010EECBGED1

DENNIS A. WICKER CIVIC CENTER

AUDITORIUM LIGHTING AND DIMMER SCOPE

SMALL AUDITORIUM SCOPE

Contractor will remove all incandescent fixtures with no replacements. All Medal Halide Fixtures will be removed and replaced with T-5 Fixtures. Conduit will be ran to fixtures for communication wires from dimming system. Conduit will be painted to match ceiling structure. Occupancy sensors will be installed above entrance doors to bring on all entrance door way lights . All T-5 lights will be controlled by dimming system. See Dimming Specs for all details and material list.

LARGE AUDITORIUM SCOPE

Contractor will remove all T-12 fixtures with no replacements. All Medal Halide Fixtures will be removed and replaced with T-5 Fixtures. Conduit will be ran to fixtures for communication wires from dimming system. Conduit will be painted to match ceiling structure. Occupancy sensors will be installed above main door ways to bring on all entrance door way lights . All T-5 lights will be controlled by dimming system. See Dimming Specs for all details and material list.